## Slide 1: Versão de: CS 152 Computer Architecture and Engineering Lecture 16: Vector Computers
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.cs.berkeley.edu/~cs152

## Slide 2: Supercomputers
Definition of a supercomputer:
Fastest machine in world at given task
A device to turn a compute-bound problem into an I/O bound problem
Any machine costing $30M+
Any machine designed by Seymour Cray
CDC6600 (Cray, 1964) regarded as first supercomputer

## Slide 3: Supercomputer Applications
Typical application areas
  Military research (nuclear weapons, cryptography)
  Scientific research
  Weather forecasting
  Oil exploration
  Industrial design (car crash simulation)
  Bioinformatics
  Cryptography
All involve huge computations on large data sets
In 70s-80s, Supercomputer  Vector Machine

## Slide 4: Vector Supercomputers
Epitomized by Cray-1, 1976:
Scalar Unit
  Load/Store Architecture
Vector Extension
  Vector Registers
  Vector Instructions
Implementation
  Hardwired Control
  Highly Pipelined Functional Units
  Interleaved Memory System
  No Data Caches
  No Virtual Memory

## Slide 5: Cray-1 (1976)
Single Port
Memory
16 banks of 64-bit words
+
8-bit SECDED
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
memory bank cycle 50 ns processor cycle 12.5 ns (80MHz)
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers

## Slide 6: Limits of Static Scheduling
Unpredictable branches
Variable memory latency (unpredictable cache misses)
Code size explosion
Compiler complexity
Despite several attempts, VLIW has failed in general-purpose computing arena.
Successful in GPU and embedded DSP market.

## Slide 7
Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Scalar Registers
r0
r15
Vector Registers
v0
v15
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load and Store Instructions
LV v1, r1, r2
Base, r1
Stride, r2
Memory
Vector Register

## Slide 8: Vector Code Example
# Scalar Code
LI R4, 64
loop:
L.D F0, 0(R1)
L.D F2, 0(R2)
ADD.D F4, F2, F0
S.D F4, 0(R3)
DADDIU R1, 8
DADDIU R2, 8
DADDIU R3, 8
DSUBIU R4, 1
BNEZ R4, loop
# Vector Code
LI VLR, 64
LV V1, R1
LV V2, R2
ADDV.D V3, V1, V2
SV V3, R3
# C code
for (i=0; i<64; i++)
C[i] = A[i] + B[i];
De loop: para baixo, todas as instruções executam 64 vezes
Todas as instruções executam apenas uma vez

## Slide 9: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive, tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in same pattern as previous operations
  access a contiguous block of memory (unit-stride load/store)
  access memory in a known pattern (strided load/store)
Scalable
  can run same code on more parallel pipelines (lanes)

## Slide 10
Vector Arithmetic Execution
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent (=> no hazards!)
V1
V2
V3
V3 <- V1 * V2
Six stage multiply pipeline

## Slide 11: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 12
Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
Base
Stride
Vector Registers
Memory Banks
Address Generator
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
  Bank busy time: Time before bank ready to accept next request

## Slide 13: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …

## Slide 14: T0 Vector Microprocessor (UCB/ICSI, 1995)
Lane
Vector register elements striped over lanes
[0]
[8]
[16]
[24]
[1]
[9]
[17]
[25]
[2]
[10]
[18]
[26]
[3]
[11]
[19]
[27]
[4]
[12]
[20]
[28]
[5]
[13]
[21]
[29]
[6]
[14]
[22]
[30]
[7]
[15]
[23]
[31]

## Slide 15: Vector Instruction Parallelism
load
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Complete 24 operations/cycle while issuing 1 short instruction/cycle

## Slide 16: Vector Chaining
Vector version of register bypassing
  introduced with Cray-1
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4

## Slide 17: Vector Chaining Advantage
With chaining, can start dependent instruction as soon as first result appears
Load
Mul
Add
Load
Mul
Add
Time
Without chaining, must wait for last element of result to be written before starting dependent instruction

## Slide 18: Vector Startup
Two components of vector startup penalty
  functional unit latency (time through pipeline)
  dead time or recovery time (time before another vector instruction can start down pipeline)
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
Functional Unit Latency
Dead Time
First Vector Instruction
Second Vector Instruction
Dead Time

## Slide 19: Dead Time and Short Vectors
Cray C90, Two lanes
4 cycle dead time
Maximum efficiency 94% with 128 element vectors
4 cycles dead time
T0, Eight lanes
No dead time
100% efficiency with 8 element vectors
No dead time
64 cycles active

## Slide 20: Vector Memory-Memory versus Vector Register Machines
Vector memory-memory instructions hold all vector operands in main memory
The first vector machines, CDC Star-100 (‘73) and TI ASC (‘71), were memory-memory machines
Cray-1 (’76) was first vector register machine
for (i=0; i<N; i++)
{
C[i] = A[i] + B[i];
D[i] = A[i] - B[i];
}
Example Source Code
ADDV C, A, B
SUBV D, A, B
Vector Memory-Memory Code
LV V1, A
LV V2, B
ADDV V3, V1, V2
SV V3, C
SUBV V4, V1, V2
SV V4, D
Vector Register Code

## Slide 21: Vector Memory-Memory vs. Vector Register Machines
Vector memory-memory architectures (VMMA) require greater main memory bandwidth, why?
  All operands must be read in and out of memory
VMMAs make if difficult to overlap execution of multiple vector operations, why?
  Must check dependencies on memory addresses
VMMAs incur greater startup latency
  Scalar code was faster on CDC Star-100 for vectors < 100 elements
  For Cray-1, vector/scalar breakeven point was around 2 elements
Apart from CDC follow-ons (Cyber-205, ETA-10) all major vector machines since Cray-1 have had vector register architectures
(we ignore vector memory-memory from now on)

## Slide 22: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252