## Slide 1: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a massive compile-time reordering of operation sequencing
 Requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 2: Vector Stripmining
Problem: Vector registers have finite length
Solution: Break loops into pieces that fit in registers, “Stripmining”

## Slide 3: Vector Conditional Execution
Problem: Want to vectorize loops with conditional code:
      for (i=0; i<N; i++)
      if (A[i]>0) then
      A[i] = B[i];
Solution: Add vector mask (or flag) registers
  vector version of predicate registers, 1 bit per element
…and maskable vector instructions
  vector operation becomes NOP at elements where mask bit is clear
Code example:
  CVM # Turn on all elements
  LV vA, rA # Load entire A vector
  SGTVS.D vA, F0 # Set bits in mask register where A>0
  LV vA, rB # Load B vector into A under mask
  SV vA, rA # Store A back to memory under mask

## Slide 4: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 5: Vector Reductions
Problem: Loop-carried dependence on reduction variables
  sum = 0;
  for (i=0; i<N; i++)
  sum += A[i]; # Loop-carried dependence on sum
Solution: Re-associate operations if possible, use binary tree to perform reduction
  # Rearrange as:
  sum[0:VL-1] = 0 # Vector of VL partial sums
  for(i=0; i<N; i+=VL) # Stripmine VL-sized chunks
  sum[0:VL-1] += A[i:i+VL-1]; # Vector sum
  # Now have VL partial sums in one vector register
  do {
  VL = VL/2; # Halve vector length
  sum[0:VL-1] += sum[VL:2*VL-1] # Halve no. of partials
  } while (VL>1)

## Slide 6: Vector Scatter/Gather
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  LV vD, rD # Load indices in D vector
  LVI vC, (rC+vD) # Load indirect from rC base
  LV vB, rB # Load B vector
  ADDV.D vA,vB,vC # Do add
  SV vA, rA # Store result

## Slide 7: Vector Scatter/Gather
Scatter example:
  for (i=0; i<N; i++)
  A[B[i]]++;
Translation (for VL elements)
  LV vB, rB # Load indices in B vector
  LVI vA, (rA+vB) # Gather initial A values
  ADDVS.D vA, vA, F0 # Increment
  SVI vA, (rA+vB) # Scatter incremented values

## Slide 8: A Modern Vector Super: NEC SX-9 (2008)
65nm CMOS technology
Vector unit (3.2 GHz)
  8 foreground VRegs + 64 background VRegs (256x64-bit elements/VReg)
  64-bit functional units: 2 multiply, 2 add, 1 divide/sqrt, 1 logical, 1 mask unit
  8 lanes (32+ FLOPS/cycle, 100+ GFLOPS peak per CPU)
  1 load or store unit (8 x 8-byte accesses/cycle)
Scalar unit (1.6 GHz)
  4-way superscalar with out-of-order and speculative execution
  64KB I-cache and 64KB data cache
(See also Cray X1E in Appendix F)
Memory system provides 256GB/s DRAM bandwidth per CPU
Up to 16 CPUs and up to 1TB DRAM form shared-memory node
  total of 4TB/s bandwidth to shared DRAM memory
Up to 512 nodes connected via 128GB/s network links (message passing between nodes)
Notes: Picture from NEC article “A hardware overview of SX-6 and SX-7 supercomputer”

## Slide 9: Multimedia Extensions (aka SIMD extensions)
Very short vectors added to existing ISAs for microprocessors
Use existing 64-bit registers split into 2x32b or 4x16b or 8x8b
  This concept first used on Lincoln Labs TX-2 computer in 1957, with 36b datapath split into 2x18b or 4x9b
  Newer designs have 128-bit registers (PowerPC Altivec, Intel SSE2/3/4)
Single instruction operates on all elements within register
16b
16b
16b
16b
32b
32b
64b
8b
8b
8b
8b
8b
8b
8b
8b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
+
+
+
+
4x16b adds

## Slide 10: Multimedia Extensions versus Vectors
Limited instruction set:
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be aligned to 64/128-bit boundary
Limited vector register length:
  requires superscalar dispatch to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors
  Better support for misaligned memory accesses
  Support of double-precision (64-bit floating-point)
  New Intel AVX spec (announced April 2008), 512b vector registers (expandable up to 1024b)

## Slide 11: Graphics Processing Units (GPUs)
Original GPUs were dedicated fixed-function devices for generating 3D graphics
More recently, GPUs have been made more programmable, so called “General-Purpose” GPUs or GP-GPUs.
Base building block of modern GP-GPU is very similar to a vector machine
  e.g., NVIDIA G80 series core (NVIDIA term is Streaming Multiprocessor, SM) has 8 “lanes” (NVIDIA term is Streaming Processor, SP). Vector length is 32 elements (NVIDIA calls this a “warp”).
Currently machines are built with separate chips for CPU and GP-GPU, but future designs will merge onto one chip
  Already happening for smartphones and tablet designs

## Slide 12: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252